AT+ADR	Get or Set the Adaptive Data Rate setting. (0: off, 1: on)
AT+APPEUI	Get or Set the Application EUI
AT+APPKEY	Get or Set the Application Key
AT+APPSKEY	Get or Set the Application Session Key
AT+BAND	Get or Set the Regional Band
AT+BAT	Get the battery level
AT+CERTIF	Set the module in LoraWan Certification Mode
AT+CFM	Get or Set the confirmation mode (0-1)
AT+CFS	Get confirmation status of the last AT+SEND (0-1)
AT+CLASS	Get or Set the Device Class
AT+CTX	send with confirmation
AT+DEV	Get the version of the AT_Slave FW
AT+DEVADDR	Get or Set the Device address
AT+DEVEUI	Get the Device EUI
AT+DFORMAT	select hex or binary format
AT+DR	Get or Set the Data Rate. (0-7 corresponding to DR_X)
AT+DUTYCYCLE	Get or Set the ETSI Duty Cycle setting - 0=disable, 1=enable - Only for testing
AT+FCD	Get or Set the Frame Counter Downlink
AT+FCU	Get or Set the Frame Counter Uplink
AT+IDNWK	Get or Set the Network ID
AT+JN1DL	Get or Set the Join Accept Delay between the end of the Tx and the Join Rx Window 1 in ms
AT+JN2DL	Get or Set the Join Accept Delay between the end of the Tx and the Join Rx Window 2 in ms
AT+JOIN	Join network
AT+MODE	Get or Set the Network Join Mode. (0: ABP, 1: OTAA)
AT+NJS	Get the join status
AT+NWK	Get or Set the public network mode. (0: off, 1: on)
AT+NWKSKEY	Get or Set the Network Session Key
AT+PORT	set application port
AT+REBOOT	Trig a reset of the MCU
AT+RECV	print last received data in raw format
AT+RECVB	print last received data in binary format (with hexadecimal values)
AT+RFPOWER	Get or Set the Transmit Power (0-5)
AT+RSSI	Get the RSSI of the last received packet
AT+RX1DL	Get or Set the delay between the end of the Tx and the Rx Window 1 in ms
AT+RX2DL	Get or Set the delay between the end of the Tx and the Rx Window 2 in ms
AT+RX2DR	Get or Set the Rx2 window data rate (0-7 corresponding to DR_X)
AT+RX2FQ	Get or Set the Rx2 window frequency
AT+SEND	Send text data along with the application port
AT+SENDB	Send hexadecimal data along with the application port
AT+SNR	Get the SNR of the last received packet
AT+TCONF	Config LORA RF test
AT+TOFF	Stops on-going RF test
AT+TRLRA	Starts RF Rx LORA test
AT+TRSSI	Starts RF RSSI tone test
AT+TTLRA	Starts RF Tx LORA test
AT+TTONE	Starts RF Tone test
AT+UTX	send without confirmation
AT+VER	Get the version of the AT_Slave FW
AT+CHANMASK	Gets the current region's channel mask, note this is reset when changing regions
AT+CHANDEFMASK	Gets the current region's default mask, note this is reset when changing regions